## Slide 1: 8086 Assembly
Problem Set 1

## Slide 2: 8086 Registers

## Slide 3: 8086 Registers

## Slide 4: 8086 Flags

## Slide 5: Little Endian vs Big Endian
In a little-endian system, the address of a given value in memory, taken as a 32-, 16-, or 8-bit width, is the same making CASTING (and Arithmetic Ops) easier.
Humans are Big Endian

## Slide 6: Physical vs Logical Address
8086 has a 16-bit Registers BUT 20-bit address bus, Why? To get 1M Memory (2 ^ 20)
Solution:
  1. Shift segment address 4-bits to the left (SHIFT BASE)
  2. Add Index address to the shifted base address (ADD OFFSET)
Example CS = 348AH, IP = 4214H then the next instruction is at
348A0H + 4214H = 38AB4H
Logical Address  segment:offset
Physical Address  absolute number
Memory in 8086 is Byte Addressable

## Slide 7: Side Note: 8086 has another ALU-ish
The feature of fetching the next instruction while the current instruction is executing is called pipelining

## Slide 8: Addressing Modes
The 8086 provides powerful instruction set with the addressing modes:
Addressing Mode | Example | Notes
Immediate | Mov AL, 20 | 
Register | Mov AL, BL | 
Direct | Mov AL, [0200] | [0200] = Content of DS:0200
Register Indirect | Mov AL, [BX] | [BX] = Content of the address in DS:BX
Based Relative | Mov AL, [BX+2] | [BX] = Content of the address in DS:(BX + 2)
Indexed Relative | Mov AL, [SI+2] | [SI] = Content of the address in SS:(SI + 2)
Based Indexed | Mov AL, [BX][SI]+2 | [BX][SI]+2 = Content of the address in DS:(BX+SI+2)

## Slide 9
Addressing Modes

## Slide 10: Problem 1
State another way to increase the processing power of the CPU other than increasing the frequency.
  Pipelining
  Increasing Number of Cores

## Slide 11: Problem 2
Which of the following instructions cannot be coded in 8086 Assembly language? Give the reason why not, if any.
a) MOV AX,27
b) MOV AL,97F
c) MOV DS,9BF2
d) MOV CX,397
  Yes
  No, Operands Size doesn’t match
  No, Invalid Operation (using immediate value with a segment register)
  Yes

## Slide 12: Problem 2
Which of the following instructions cannot be coded in 8086 Assembly language? Give the reason why not, if any.
e) MOV 81,9516
f) MOV CS,3490
g) MOV DS,BX
h) MOV BX,CS
  Yes, 9516 is moved to DS:0081 (TESTED OK)
  No, No, Invalid Operation (using immediate value with a segment register)
  Yes
  Yes

## Slide 13: Problem 2
Which of the following instructions cannot be coded in 8086 Assembly language? Give the reason why not, if any.
i) MOV CH,AX
j) MOV AX,23FB9
k) MOV CS,BH
l) MOV AX,DL
  No, operands do not match: 8 bit and 16-bit register
  No, no 'h' suffix; or unmatched operands
  No, operands do not match: 8 bit and 16-bit register
  No, operands do not match: 16-bit and 8-bit register

## Slide 14: Problem 3
If an instruction that needs to be fetched is in physical memory location 389F2 and CS = 2700, does the code segment range include it or not?
CS range is
CS Lower = 27000 + 0000 = 27000
CS Higher = 27000 + FFFF = 36FFF
Then 389F2 is not in the range

## Slide 15: Problem 3
If an instruction that needs to be fetched is in physical memory location 389F2 and CS = 2700, does the code segment range include it or not? If not, what value should be assigned to CS if the IP must be = 1282?
CS x 10 + 1282 = 389F2
CS x 10 = 389F2 – 1282 = 37770
Then CS = 3777

## Slide 16: Problem 4
Assume that SP = FF2EH, AX = 3291H, BX = F43CH, and CX = 09. Find the content of the stack and stack pointer after the execution of each of the following instructions.
PUSH AX
PUSH BX
POP AX
PUSH CX
POP BX

## Slide 17: 8086 Stack
STACK
00010101
00000000
Single Word
8 - bits
Stack is Byte - Addressable
FFFF
0000
PUSH a Register (Word)
SP = SP - 2
POP a Register (Word)
SP = SP + 2

## Slide 18: Problem 4
Assume that SP = FF2EH, AX = 3291H, BX = F43CH, and CX = 09. Find the content of the stack and stack pointer after the execution of each of the following instructions.
PUSH AX
PUSH BX
POP AX
PUSH CX
POP BX
 | Stack [Empty] | SP [FF2EH]
PUSH AX | FF2D  32 FF2C  91 | FF2C
PUSH BX | FF2D  32 FF2C  91 FF2B  F4 FF2A  3C | FF2A
POP AX | FF2D  32 FF2C  91 | FF2C
PUSH CX | FF2D  32 FF2C  91 FF2B  00 FF2A  09 | FF2A
POP BX | FF2D  32 FF2C  91 | FF2C
STACK GROWS DOWNWARD

## Slide 19: Problem 5
What is the function of the following code?
  PUSH AX
  PUSH BX
  POP AX
  POP BX
Swap AX, BX  XCHG AX, BX

## Slide 20: Problem 6
What is the main disadvantage of using the stack as temporary storage compared to having a large number of registers inside the CPU?
The main disadvantage is that it’s in memory, and memory is slower than CPU registers in a variety of ways. It usually has longer latency and lower bandwidth. Memory accesses are harder to speed up.

## Slide 21: Problem 7 - a
Find the status of the CF, PF, AF, ZF, and SF for the following operations.
MOV BL,9FH
ADD BL,61H
 | CF | PF | AF | ZF | SF | OF
MOV BL, 9FH | 0 | 0 | 0 | 0 | 0 | 0
ADD BL, 61H | 1 | 1 | 1 | 1 | 0 | 0
Note: OF flag works in case of Signed operations only
(when carry is from 7th bit to 8th bit or 15th to 16th)
Steps Required

## Slide 22: Problem 7 - b
MOV AL,23H
ADD AL,97H
Find the status of the CF, PF, AF, ZF, and SF for the following operations.
 | CF | PF | AF | ZF | SF | OF
MOV AL, 23H | 0 | 0 | 0 | 0 | 0 | 0
ADD AL, 97H | 0 | 0 | 0 | 0 | 1 | 0

## Slide 23: Problem 7 - c
 | CF | PF | AF | ZF | SF | OF
MOV DX, 10FFH | 0 | 0 | 0 | 0 | 0 | 0
ADD DX, 1 | 0 | 1 | 1 | 0 | 0 | 0
MOV DX,10FFH
ADD DX,1
Find the status of the CF, PF, AF, ZF, and SF for the following operations.

## Slide 24: Problem 8
Assume that the registers have the following values (all in hex)
  Calculate the physical address of the memory where the operand is stored and the contents of the memory locations in each of the following addressing examples.
CS = 1000 | AX = 25FF | SI = 4000
DS = 2000 | BX = 6080 | DI = 5000
SS = 3000 | CX = 8791 | 
ES = 9000 | DX = 1299 | 

## Slide 25: Problem 8
Note: The Question covers two points
Which segment to use as base address?
What value to use? How many bytes?

## Slide 26
MOV [SI], AL
Reference by DS
DS:SI
Physical memory location = 20000 + 4000 = 24000
24000  FF
Problem 8
CS = 1000 | AX = 25FF | SI = 4000
DS = 2000 | BX = 6080 | DI = 5000
SS = 3000 | CX = 8791 | BP = 7000
ES = 9000 | DX = 1299 | 

## Slide 27: Problem 8
Reference by DS
Physical memory location = 20000 + 4000 + 6080 + 8 = 2A088
2A088  25
MOV [BX], AX
Reference by DS
Physical memory location = 20000 + 6080 = 26080
26080  FF
26081  25
MOV [SI+BX+8], AH
CS = 1000 | AX = 25FF | SI = 4000
DS = 2000 | BX = 6080 | DI = 5000
SS = 3000 | CX = 8791 | BP = 7000
ES = 9000 | DX = 1299 | 

## Slide 28: Problem 8
Reference by DS
Physical memory location = 20000 + 5000 + 6 = 25006
25006  80
25007  60
MOV [BX][DI]+28, CX
Reference by DS
Physical memory location = 20000 + 6080 + 5000 + 28 = 2B0A8
2B0A8  91
2B0A9  87
CS = 1000 | AX = 25FF | SI = 4000
DS = 2000 | BX = 6080 | DI = 5000
SS = 3000 | CX = 8791 | BP = 7000
ES = 9000 | DX = 1299 | 
MOV [DI+6], BX

## Slide 29: Problem 8
Reference by SS
Physical memory location = 30000 + 7000 + 4000 + 10 = 3B010
3B010  99
3B011  12
CS = 1000 | AX = 25FF | SI = 4000
DS = 2000 | BX = 6080 | DI = 5000
SS = 3000 | CX = 8791 | BP = 7000
ES = 9000 | DX = 1299 | 
MOV [BP][SI]+10, DX